## Slide 1: Accel Mouse
Philipp Ahrendt, Christian Siman, Song xxx
Robotics Project

## Slide 2: Introduction
Build a robotic application
Use sensors to estimate position or attitude of object
Our phones have the common sensors most robots use
  Accelerometer
  Gyrometer
  Magnetometer

## Slide 3: First try
Use mouse on the table (with a sliding case) similar to a regular mouse
Assumption:
  Use our sensors to estimate delta x & y (change in position)
    Gyrometer and magnetometer don’t help for this
    So only Accelerometer is left
      Problem: sensor fusion is not possible with one sensor and most estimation get a lot more robust with at least two sensors
    Technically you could still compute the delta by double integration of accelerometer data
      Problem: there is noise in the sensor so with integration there is a drift over time between the actual and estimated velocity
      Integrating the velocity to get the position increases the drift even more

## Slide 4: Structure
Picture of Server and Client (Phone)

## Slide 5: Structure
Server
  Handling the incoming data
  Maps pitch and yaw attitude to pixels of display
  Controls the mouse through a <python> library with calculated pixels as destination input
iPhone as client
  Swift library to get the accelerometer, magnetometer and gyrometer data
  Calculate roll from accelerometer data <insert formula>
  Calculate yaw from gyroscope data with numerical integration <insert formula>
Notes: Could not use magnetometer data because the calculation did not return correct results

## Slide 6: Mechanics
Picture of screen and pitched phone showing displacement on y-axis
  Show corresponding angle values and pixel values
Picture of screen and rotated phone showing displacement on x-axis

## Slide 7
Switch to code
Notes: Switch to code

## Slide 8: Filter
Pitch complimentary filter
Yaw filter was impossible since we could only use one sensor
No need to use quaternions since we do not need the 90° degree pitch angle and do not use the magnetometer

## Slide 9: References

## Slide 10: Thank you!
Questions?